## Slide 1: Research Practice Learning

## Slide 2
Parallel Computing: In parallel computing multiple processors performs multiple tasks assigned to them simultaneously. Memory in parallel systems can either be shared or distributed. Parallel computing provides concurrency and saves time and money.
Distributed Computing: In distributed computing we have multiple autonomous computers which seems to the user as single system. In distributed systems there is no shared memory and computers communicate with each other through message passing. In distributed computing a single task is divided among different computers.

## Slide 3
Efficient task scheduling has always been one of the most critical issues for high performance in heterogeneous computing. The heterogeneity of computation costs on a given set of processors and the communication costs among processors increase the complexity of the scheduling problem. Generally, the application consists of several tasks with dependencies. If the computation costs, task dependencies and communication costs are known a priori, the application can be represented by a static model, namely the directed acyclic graphs (DAG) model.

## Slide 4
Task scheduling methods aim to minimize the overall time of completion (makespan)
Task duplication based scheduling algorithms generate shorter schedules without sacrificing efficiency but leave the computing resources over consumed due to the heavily duplications.
try to optimized by removing some duplicated tasks in the schedule whose removal does not affect the makespan adversely.

## Slide 5: MultiProcessor Architectures
Systems on chip (SOC) contain multiple concurrent applications with different time criticality (firm, soft, non real-time). As a result, they are often developed by different teams or companies, with different models of computation (MOC) such as dataflow, Kahn process networks (KPN), or time-triggered (TT). SOC functionality and (real-time) performance is verified after all applications have been integrated.
In this paper we propose the CompSOC platform and design flows that offers a virtual execution platform per application, to allow independent design, verification, and execution. We introduce the composability and predictability concepts, why they help, and how they are implemented in the different resources of the CompSOC architecture. We define a design flow that allows real-time cyclo-static dataflow (CSDF) applications to be automatically mapped, verified, and executed. Mapping and analysis of KPN and TT applications is not automated but they do run composably in their allocated virtual platforms.
Although most of the techniques used here have been published in isolation, this paper is the first comprehensive overview of the CompSOC approach. Moreover, three new case studies illustrate all claimed benefits: 1) An example firm-real-time CSDF H.263 decoder is automatically mapped and verified. 2) Applications with different models of computation (CSDF and TT) run composably. 3) Adaptive soft-real-time applications execute composably and can hence be verified independently by simulation.